## Slide 1
Data Modes for Emergency Communications
Clint Miller KCØJUO, COML
Story County ARES
October 5th, 2017

## Slide 2
Digital vs. Data
Digital modes could mean voice or data
There are non-digital data modes
Using “data modes” clears up any confusion

## Slide 3
Communication Modes
Communication modes fall into several categories:
  Point to point -- Telephone, fax, radio voice and data
  Multi-point – Radio voice, CW, and data modes
  High precision -- Fax, e-mail, radio data modes
  Low precision -- Radio voice and CW, telephone
  High priority -- Radio voice, telephone
  Low priority -- Fax, e-mail, radio data modes and CW

## Slide 4
Message Categories
Message types fall into similar categories:
  Point to point -- Messages intended for one party
  Point to multi-point -- Messages intended for a group
  Multi-point to point -- Messages from members of a group directed to one station
  High precision -- Lists of items, medical or technical terminology, specialized or detailed information
  Low precision -- Traffic reports, damage estimates, simple situation reports
  High priority -- Fast delivery is critical
  Low priority -- Messages can be delivered in a more relaxed time frame

## Slide 5
Voice vs. Data
Voice modes are ideal for low-precision messages
  Tactical
  Time-critical
  Could be formal written traffic
Data modes facilitate high-precision message transfer
  Roster of evacuees
  Prescription medication request
  Directions through a disaster scene
  Situation report
  Lists and detailed messages

## Slide 6
Why Data EmComm?
The needs of our Served Agencies have changed
They still need voice communications but...
There's an increasing need for data communications
We need to be able to provide more than just voice communications with an HT
Remember data modes are not secure
Most appropriate method might be hand delivery by a radio-dispatched courier

## Slide 7
Why Data EmComm?
Some data modes provide virtually error-free transmission
Relays can be accomplished by retransmitting the received data message without having to retype
Documentation and printing of message text
Record of when message was sent / received

## Slide 8
Historic Progression of Data Modes for EmComm
CW (and high-speed CW)
RTTY (Radio TeleTYpe)
AMTOR (error-correction for amateur RTTY)
Packet (AX.25 protocol – requires TNC)
PACTOR (hardware modem)
APRS (Automatic Packet Reporting System)
Sound Card Modes (including PSK, FSK, MFSK, etc…)
  Sound card software allows rapid mode experimentation and development

## Slide 9
Historic Progression of Data Modes for Emergency Communications
The trend has been to modes with:
  Higher bitrates
  Better copy with lower signal to noise (robust)
  Automatic error correction techniques

## Slide 10
Requirements for
HF Data Modes
Noise and interference tolerant
Good weak signal performance
Error correction techniques
  FEC, ARQ, interleaving, et al
In a word… ROBUST!

## Slide 11
What HF Modes
Are Available?
“QSO” modes – not well-suited to EmComm
  BPSK31, RTTY, others
More robust modes
  MFSK16, MT63, Olivia, PACTOR, and more
“Interesting” modes
  JT9, JT65, MSK144, FT8

## Slide 12
Winlink
Not a mode…
  Method of interconnected messaging
  Worldwide “hybrid” email network
Utilizes multiple different data modes
  WINMOR
  PACTOR
  D-Star
  AX.25 packet (300 baud limit on HF)
  802.11 (Wi-Fi)
  TCP/IP (including telnet)

## Slide 13
Winlink
Numerous Radio Mail Server (RMS) stations maintained on a volunteer basis by licensed amateurs
Each RMS station is connected through the Internet (Telnet) to Winlink system
  Network of 5 redundant Common Message Servers
  "CMS"
RMS Express recommended interface
  Provides a complete email messaging system

## Slide 14
Winlink on VHF/UHF
VHF/UHF packet radio gateways to the system
Automated messaging using 1200 baud AX.25 packet
  Now integrated into RMS Express software
  Soundcard access using UZ7HO SoundModem
  Not using AGWPE any more
Ideal to provide a temporary portable or fixed emergency portal for radio e-mail users
Can do one-to-one connections

## Slide 15
Images and Video
Amateur TV
  Slow-scan for photos
  Fast-scan for video
High Speed Multimedia
  Voice over Internet protocol (VoIP)
  Cameras
  Instant messaging
  Video conferencing
  Remote station control
  Repeater linking
  Send real-time video and data files

## Slide 16
High Speed Multimedia
802.11
Mesh Networking
Broadband-Hamnet
AREDN
  Amateur Radio Emergency Data Network
  Uses new, off-the-shelf equipment
  2 channels on 2.4 GHz
  24 channels on 3.4 GHz
  7 channels on 5.8 GHz
  Can use public channels but they are crowded!

## Slide 17
Automatic Link Establishment (ALE)
Method for digitally initiating and sustaining HF radio communications
Avoids guesswork, beacon listening, and complicated HF prediction charts
  Each HF SSB transceiver constantly scans through list of frequencies, listening for its callsign / address
  On schedule, transceiver transmits its station ID
  Local system records best paths between stations
  Operator enters callsign, system chooses best path, and software connects the stations
http://hflink.com

## Slide 18
Why should we focus on VHF/UHF?
Most probable communications emergency scenario will be exclusively local
“Last Mile” communications are our most likely role
HF ground wave or NVIS could be an option
VHF/UHF simplex or repeaters will usually be able to address “Last Mile” needs
Nearly every ham owns a VHF/UHF radio
Technicians aren’t excluded

## Slide 19
VHF/UHF Modes
Most popular ones are...
  MT63 (500, 1000, 2000 long)‏
  Olivia
  Domino
  “R” PSK modes...fast with FEC
  PSK31
    Good for making non-emcomm contacts
    No error correction

## Slide 20
High-Speed Modes
Fast modes now available:
  PSK-125R
  PSK-250R
  PSK-500R
“R” signifies Robust
Contains Forward Error Correction (FEC)
PSK-500R is approximately twice as fast as MT63-2000

## Slide 21
High-Speed
Multi-Carrier Modes
Multi-psk modes now available
  PSK signals sent in parallel, up to 12 carriers
  Can have parallel PSK and PSKR modes
  Blazingly fast
  Must trade off speed vs robustness
Good compromise mode...PSK125R x 5
Modes of multi 500 Hz wide carriers not legal on HF

## Slide 22
ARES Software Standards?
There are NO national or Iowa messaging and software standards
Local ARES groups can decide which modes, bands, or software fits their needs
Some groups have chosen:
  Winlink
  NBEMS
  Packet
Most groups have
  no official system
  don’t offer data messaging

## Slide 23
Equipment for
Data Messaging
Radio to receive and transmit
  Just about any radio will due for testing and practice
  Watch duty cycles and battery life
  Data jacks to allow easier interfacing
Interface from radio to computer
  SignaLink USB
  Rigblaster
  Homebrew interface
  Keying circuit or VOX
  Acoustical coupling

## Slide 24
Equipment for
Data Messaging
Computer to decode and display messages
  PC or laptop
  Linux or Android single board computer
  Tablet or phone
Software to compose and decode messages
Printer
Scanner

## Slide 25
Software Options
APRS
ATV
Packet
Winlink
NBEMS (Fldigi)

## Slide 26
Narrow Band Emergency Messaging System
Consists of multiple programs:
  Fldigi – Fast Light Digital modem application
  Flwrap – embed a checksum in a file
  Flmsg – easily send ICS forms and Radiograms
  Flarq – automatic repeat requests (ARQ)
  Can download from www.w1hkj.com
Runs on Windows (XP or newer), Linux, Mac
  Android using AndFlmsg app
Open Source, released under GNU Public License, it is completely FREE

## Slide 27
Western Pennsylvania ARES
Using NBEMS extensively
Published standards online
Great template to design our own local standards for data messaging
Included standards
  Modes
  File verification
  Transmission of binary files
  Formal VHF/UHF and HF net procedures
wpaares.org/html/nbems.html

## Slide 29
Western Pennsylvania ARES
Standard Modes
VHF/UHF FM
  MT63-2000 long
HF Keyboard Chat
  Olivia 8/500 - good conditions
  Olivia 16/500 - bad conditions
HF Bulletins
  MT63-1000 - good conditions
  MT63-500 - bad conditions

## Slide 30
Fldigi

## Slide 31
How it works
Fldigi uses your computer's sound card to generate and decode data signals
  SignaLink adds separate sound card and VOX
All work is done by your computer, no external Terminal Node Controller (TNC)
Audio from your computer speakers go into your radio's mic input for transmission
Audio from your radio goes into your computer's mic or line-in for decoding
Don't need an extremely powerful new computer, older machines work just fine

## Slide 32
Convert from Contest Mode to Message Mode
Load messaging specific macros
Turn on RSID transmit and receive
  Configure>IDs
  Check Searches passband
  Add a Pre-Signal Tone of 1 or 2 seconds
Start New Modem at Sweet Spot unchecked
  Configure->Defaults->Misc
Configure>Save Config
Set up multiple Fldigi configurations!

## Slide 33
Flmsg – Send/Receive Messages
Flmsg used to send formatted messages:
  ICS forms like ICS-213
  ARRL Radiograms
  Blank text
Easy workflow for CSV spreadsheets
Starts transmission automatically
Eases importing and checksum verification of incoming message
Can have incoming messages automatically opened

## Slide 34
Flmsg Screenshot

## Slide 35
Data Verification with Checksums
Checksums allow you to be 100% sure your message was received accurately
Checksum is inserted into a file by Flmsg
Receiving station computes the checksum on the incoming file and...
If the two checksums are identical, the file was received without error
Allows multiple stations to receive and confirm data 100%
Great for bulletins like situation updates, weather reports, road closures, lists of contact info

## Slide 36
Example
This is an example of a file with a checksum:
[WRAP:beg][WRAP:crlf][WRAP:fn example.txt]This is an example of a wrapped file.
Here's what happens when we wrap something.[WRAP:chksum B71E][WRAP:end]
Note the WRAP beg and end delimiters
Also note the checksum, it's B71E
Flmsg automatically generates checksums
Flmsg also computes checksums on incoming messages

## Slide 37
Flmsg – AutoSend Workflow
One click sending
Enter text directly into large empty box
Can also drag-and-drop text file into box
Push the AutoSend menu at top
Will be prompted to save file with automatically assigned unique filename
Flmsg will cause Fldigi to automatically send message

## Slide 38
Flmsg Auto Display of Messages
Incoming messages can be automatically opened in Flmsg
Can also auto open messages in browsers
Can walk away and come back to see messages displayed
Display in browser great for EOC or served agency facility
Email or print for delivery

## Slide 39
Flmsg – Send ICS-213 and ARRL Radiogram
Flmsg is a powerful tool in NBEMS
Can send ICS, ARRL Radiogram, Red Cross and Hospital forms
ICS forms include (not complete list):
  ICS-203 Organization Assignment List
  ICS-205 Incident Radio Communications Plan
  ICS-213 General Message (most common)
  ICS-214 Unit Log
Can send and receive files very easily with 100% verification

## Slide 40
ICS-213 in HTML

## Slide 41
Flmsg – Radiogram HTML Format

## Slide 42
Flmsg Custom Templates
Say you need a standard report for...
  Hospital bed count
  Shelter info
  Resource request
  Situation report (sitrep)
Flmsg supports custom templates
Distribute before event, or even over the air
Import template into Flmsg, fill it out and transmit
  Windows: User > NBEMS files > CUSTOM
Use Template menu to save and load

## Slide 43
Flmsg Templates

## Slide 44
Story EMA Sitrep Template
Started with standard Situation Report format from Story County EMA
KCØEDE converted to an HTML document
Without formatting, text file is much smaller
Smaller means faster
Distribute before event or disaster
  Possible to send over air if necessary
http://storyares.org/downloads
  Story County EMA SITREP for NBEMS – DRAFT

## Slide 47
Data Guidelines for NBEMS
Send only text files, no binary files
Do not send Word Documents, save as text
Excel spreadsheets must be exported as CSV
Do not send images
Limit file size to avoid repeater timeouts
CRITICAL: Meet with Served Agency beforehand to set expectations
Encourage Served Agency to give us data electronically
Remember, we have limited bandwidth

## Slide 48
Resources
Story County ARES
  http://storyares.org/
High Speed Multimedia for Amateur Radio
Get on the Air with HF Digital

## Slide 49
Resources
ARRL's Public Service Handbook
NBEMSham Yahoo group
Western PA ARES NBEMS Website: http://wpaares.org/html/nbems.html
  User Guides and examples

## Slide 50
Resources
W1HJK (author of Fldigi) http://www.w1hkj.com/
QST Articles
  April 2008
  August 2009
  September 2013
ARRL NBEMS page http://www.arrl.org/nbems

## Slide 51
ARRL Technical Descriptions
FCC rules § 97.309(a)(4) calls for technical characteristics
  (4) An amateur station transmitting a RTTY or data emission using a digital code specified in this paragraph may use any technique whose technical characteristics have been documented publicly, such as CLOVER, G-TOR, or PacTOR, for the purpose of facilitating communications.
http://www.arrl.org/technical-characteristics

## Slide 53
IA ARES Digital Net
Tuesdays 7:00 pm
3.5725 MHz +/- USB
Olivia 8/500

## Slide 54
Final Thoughts
Learn HF modes (especially Winlink) if you have national deployment aspirations
Building our response capabilities around NBEMS on VHF/UHF
  We plan to develop and publish standards
  Use WPA ARES standards for now
  Until standards are defined, experiment until you find what works
  Upcoming NBEMS Workshop
  Establish data net on local repeater
Data modes with no automatic error correction should only be used when clean and interference-free signals can be guaranteed